## Slide 1
Prof. Swati Sharma
swati.sharma@darshan.ac.in
Microprocessor & Interfacing - 2150707 Darshan Institute of Engineering & Technology
Unit-6
Stack & Subroutines

## Slide 2: Subject Overview
Sr. No. | Unit | % Weightage
1 | Introduction to Microprocessor | 8%
2 | Microprocessor Architecture and Operations | 7%
3 | 8085 Microprocessor | 10%
4 | Assembly Language Basics | 10%
5 | 8085 Assembly Language Programs | 10%
6 | Stack & Subroutines | 10%
7 | I/O Interfacing | 15%
8 | Advanced Microprocessors | 20%
9 | SUN SPARC Microprocessor | 5%
10 | ARM Processor | 5%

## Slide 3: Stack
Stack is a group of memory location in the R/W memory that is used for temporary storage of binary information during execution of a program.
The starting memory location of the stack can be defined in program and space is reserved usually at the high end of memory map.
E.g.: LXI SP,FFF8; loads 16-bit memory address in stack pointer

## Slide 4: Stack
Instruction necessary for stack are as follows:
LXI SP, 2095 | Load the stack pointer register with a 16-bit address.
POP B/D/H | It copies content of top two memory locations of the stack in to specified register pair
PUSH B/D/H | It copies contents of register pair on the stack
PUSH PSW | Operand PSW represents Program status word meaning. i.e. content of accumulator and flags.
POP PSW | It copies content of top two memory locations of the stack in to accumulator and flags respectively.

## Slide 5: Subroutine
A subroutine is a group of instruction that performs a subtask of repeated occurrence.
A subroutine can be used repeatedly in different locations of the program.

## Slide 6: Subroutine
Advantage of using Subroutine
Rather than repeat the same instructions several times, they can be grouped into a subroutine that is called from the different locations.
Where to write Subroutine?
In Assembly language, a subroutine can exist anywhere in the code.
However, it is customary to place subroutines separately from the main program.

## Slide 7: Subroutine
The 8085 has two instructions for dealing with subroutines.
The CALL instruction is used to redirect program execution to the subroutine.
The RET instruction is used to return.

## Slide 8: CALL Instruction
When CALL instruction is fetched, the microprocessor knows that the next two new Memory location contains 16-bit subroutine address.
Microprocessor reads subroutine address from the next two memory location and stores the higher order 8-bit of the address in the W register and stores the lower order 8bit of the address in the Z register.
Push the Older address of the instruction immediately following the CALL onto the stack [Return address].
Loads program counter(PC) with the new 16-bit address supplied with the CALL instruction from WZ registers.

## Slide 9: Working of CALL Instruction
Before CALL instruction
CALL 4 0 5 0
03
06
W
Registers
Z
PC
2 4
06
2 1
5 0
SP
Stack
0 0
SP
SP
4 0
5 0

## Slide 10: Subroutine
Working of CALL and RET instruction
Before CALL instruction
CALL 4 0 5 0
03
06
W
Registers
Z
PC
2 4
2151
2150
2149
2148
2147
2146
2145
2144
06
2 1
5 0
Stack
0 0
SP
4 0
5 0

## Slide 11: Subroutine
Working of RET instruction
RET
03
06
W
Registers
Z
PC
2 4
2151
2150
2149
2148
2147
2146
2145
2144
06
2 1
5 0
Stack
0 0
SP
SP
SP
Retrieve the return address from the top of the stack
Load the program counter with the return address.

## Slide 12: Subroutine
Things to be considered in Subroutine
Number of PUSH and POP instruction used in the subroutine must be same, otherwise, RET instruction will pick wrong value of the return address from the stack and program will fail.

## Slide 13: Counters and Time Delays

## Slide 14: Counters and Time Delays
Counters and Time Delays are important techniques.
Applications of Counters and Time Delays
They are commonly used in
Traffic Signal
Digital Clocks
Process Control
Serial data transfer

## Slide 15: Counters and Time Delays
A counter is designed simply by loading appropriate number into one of the registers and using INR or DCR instructions.
Loop is established to update the count.
Each count is checked to determine whether it has reached final number ;if not, the loop is repeated.

## Slide 16: Counters
How to create counters?
Initialize
Display
Update
Is this Final Count
YES
NO
MVI C,05
LOOP: MOV A,C
OUT 01
DCR C
JNZ LOOP
HLT
End

## Slide 17: Counters
Label | Opcode | Operand | Comment | T-states
 | MVI | C,05h | ; Load Counter | 7
 | JNZ | LOOP | ; Jump back to Decr. C | 10/7
LOOP: | DCR | C | ; Decrement Counter | 4
MVI C, 05h
Machine Cycle: F + R = 2
T-States: 4T + 3T = 7T
DCR C
Machine Cycle: F = 1
T-States: = 4T
JNZ LOOP (true)
Machine Cycle: F + R + R =3
T-States: 4T + 3T + 3T=10T
JNZ LOOP (false)
Machine Cycle: F + R = 2
T-States: 4T + 3T =7T

## Slide 18: Counters and Time Delays
Instruction MVI C, 05h requires 7 T-States to execute.
Assuming, 8085 Microprocessor with 2MHz clock frequency.
How much time it will take to execute above instruction?
Clock frequency of the system (f)= 2 MHz
Clock period (T) = 1/f = ½ * 10-6 = 0.5 s
Time to execute MVI = 7 T-states * 0.5 s
= 3.5 μs
How much time it will take to execute above instruction with 1 MHz clock frequency?

## Slide 19: Counters and Time Delays
Now to calculate time delay in loop, we must account for the T-states required for each instruction, and for the number of times instructions are executed in the loop.
The for the next two instructions:
DCR: 4 T-States
JNZ : 10 T-States
14 T-States
Here, the loop is repeated for 5 times.
Label | Opcode | Operand | Comment | T-states
 | MVI | C,05h | ; Load Counter | 7
 | JNZ | LOOP | ; Jump back to Decr. C | 10/7
LOOP: | DCR | C | ; Decrement Counter | 4


## Slide 20: Counters and Time Delays
How to calculate time delay for given loop?
Time delay in loop TL with 2MHz clock frequency is calculated as:
TL= T * Loop T-states * N10 -----------------(1)
TL : Time Delay in Loop
T : Clock Period
N10 : Equivalent decimal number of hexadecimal count loaded in the delay register
Substituting value in equation (1)
TL= (0.5 * 10-6 * 14 * 5)
= 35 s

## Slide 21: Counters and Time Delays
If we want to calculate delay more accurately, we need to accurately calculate execution of JNZ instruction
i.e
If JNZ = true, then T-States = 10
Else if JNZ =false, then T-States = 7

## Slide 22: Counters and Time Delays
Now, according to our program:
Therefore, there is difference of (10T – 7T) 3T-states:
MVI C,05
LOOP: DCR C
JNZ LOOP
HLT
Here, the last cycle will be executed in 7 T-States;
when JNZ = false

## Slide 23: Counters and Time Delays
Therefore, there is difference of (10T – 7T) 3T-states:
Delay generated by last clock cycle:
= 3T * Clock Period
= 3T * (1/2 * 10-6 )
= 1.5 s
Now, the accurate loop delay is:
TLA=TL - Delay generated by last clock cycle
= 35 s - 1.5 s
= 33.5 s
TL= (0.5 * 10-6 * 14 * 5)= 35 s

## Slide 24: Counters and Time Delays
Now, to calculate total time delay
Total Delay = Time taken to execute instruction outside loop
+
Time taken to execute loop instructions
TD = TO + TLA
= (7 * 0.5 s) + 33.5 s
= 3.5 s + 33.5 s
= 37 s

## Slide 25: Counters and Time Delays
Calculate time delay and accurate time delay for given loop with
Counter value =255 (FF h) and
Clock frequency =2MHz
TL= T * Loop T-states * N10 -----------------(1)
= 0.5 *10-6* 14* 255
= 1785 μs = 1.8 ms
TLA= Time to execute loop instructions
= TL – (3T states*clock period)
= 1785 – ( 3 * ½ * 10-6)
= 1785 – 1.5=1783.5 μs
Notes: Time Delay in Loop TL= T*Loop T states * N10
= 0.5 * 14* 255
= 1785 μs = 1.8 ms

## Slide 26: Exercise
How much time the 8085 microprocessor will take to execute the MOV B, A instruction, if the crystal frequency is 4MHz?
How much time will be required to execute the STAX B instruction if the clock frequency is 4 MHz?
How much time will be required to execute the MVI M,25h instruction if the clock frequency is 6 MHz?

## Slide 27: Time Delay using a Register Pair
Time delay can be considerably increased by setting a loop and using a register pair with a 16-bit number (FFFF h).
A 16-bit is decremented by using DCX instruction.
Problem with DCX instruction
DCX instruction doesn’t set Zero flag.
Without test flag, Jump instruction can’t check desired conditions.
Additional technique must be used to set Zero flag.

## Slide 28: Time Delay using a Register Pair
Label | Opcode | Operand | Comment | T-states
 | LXI | B,2384 h | ; Load BC with 16-bit counter | 10
 | MOV | A, C | ; Place contents of C in A | 4
LOOP: | DCX | B | ; Decrement BC by 1 | 6
 | ORA | B | ; OR B with C to chk Zero flag | 4
 | JNZ | LOOP | ; if result not equal to 0, 10/7 jump back to loop | 10/7
Here the loop includes four instructions:
Total T-States = 6T + 4T + 4T + 10T
= 24 T-states

## Slide 29: Time Delay using a Register Pair
The loop is repeated for 2384 h times.
Converting (2384)16 (_____)10
2384 h = (2 * 163 )+ (3* 162) + (8 * 161) + (4 * 160)
= 8192 + 768 + 128 + 4
= 9092
Clock frequency of the system (f)= 2 MHz
Clock period (T) = 1/f = ½ * 10-6 = 0.5 s
9092

## Slide 30: Time Delay using a Register Pair
Now, to find delay in the loop
TL= T * Loop T-sates * N10
= 0.5 *10-6* 24 * 9092
= 109104 s
= 109 ms (without adjusting last cycle)

## Slide 31: Time Delay using a LOOP within a LOOP
Label | Opcode | Operand | T-states
 | MVI | B,38h | 7T
LOOP2: | MVI | C,FFh | 7T
 | DCR | B | 4T
LOOP1: | DCR | C | 4T
 | JNZ | LOOP1 | 10/7 T
 | JNZ | LOOP2 | 10/7 T
38 h
FF h

## Slide 32: Time Delay using a LOOP within a LOOP
Calculating delay of inner LOOP1: TL1
Is Register
C = 0?
Decrement Register C
No
Yes
LOOP1
Label | Opcode | Operand | T-states
LOOP1: | DCR | C | 4T
 | JNZ | LOOP1 | 10/7 T
TL= T * Loop T-states * N10
= 0.5 *10-6* 14* 255
= 1785 μs = 1.8 ms
TL1= TL – (3T states* clock period)
= 1785 – ( 3 * ½ * 10-6)
= 1785-1.5=1783.5 μs
Delay of Loop1 TL1= 1783.5 μs

## Slide 33: Time Delay using a LOOP within a LOOP
Now, Calculating delay of outer LOOP2: TL2
TL1 Delay in LOOP1
MVI C, FF
DCR B
JNZ LOOP2
Label | Opcode | Operand | T-states
 | MVI | B,38h | 7T
LOOP2: | MVI | C,FFh | 7T
 | DCR | B | 4T
Delay of Loop1 TL1= 1783.5 μs
 | JNZ | LOOP2 | 10/7 T
Counter B : (38)16 = (56)10
Loop2 is executed for 56 times
T-States = 7 + 4 + 10 = 21 T-States
TL2 = 56 (TL1 + 21 T-States * 0.5)
= 56( 1783.5 μs + 10.5)
= 100464 μs
TL2 = 100.46 ms

## Slide 34: Disadvantage of using software delay
Accuracy of time delay depends on the accuracy of system clock.
Microprocessor is occupied simply in a waiting loop; otherwise it could be employed to perform other functions.
The task of calculating accurate time delays is tedious.
In real time applications timers are commonly used.
Intel 8254 is a programmable timer chip, that can be interfaced with microprocessor to provide timing accuracy.
The disadvantage of using hardware chip include the additional expense and the need for extra chip in the system.

## Slide 35: Counter design with time delay
Initialize Counter
Yes
No
Display
Time Delay
Update Count
Is Count
Complete?
Load Delay Register
Decrement Delay Register
Is Delay Register = 0?
Yes
No

## Slide 36: Hexadecimal counter program
Write a program to count continuously in hexadecimal from FFh to 00h with 0.5 s clock period. Use register C to set up 1ms delay between each count and display the number at one of the output port.
Given:
Counter= FF h
Clock Period T=0.5 s
Total Delay = 1ms
Output:
To find value of delay counter

## Slide 37: Hexadecimal counter program
Program
MVI B,FF
LOOP:MOV A,B
OUT 01
MVI C, COUNT; need to calculate delay count
DELAY: DCR C
JNZ DELAY
DCR B
JNZ LOOP
HLT

## Slide 38: Hexadecimal counter program
Delay Calculations
MVI B,FF;
LOOP:MOV A,B
OUT 01
MVI C, COUNT
DELAY: DCR C
JNZ DELAY
DCR B
JNZ LOOP
HLT
Instruction | T-States
Total | 14 T
DCR C | 4
JNZ DELAY | 10
Calculate Delay for Internal Loop
TI = T-States * Clock Period * COUNT
= 14 * 0.5 * 10-6 * COUNT
TI = (7.0 * 10-6 )* COUNT

## Slide 39: Hexadecimal counter program
Calculate Delay for Outer Loop:
TO = T-States * Clock Period
= 35 * 0.5 * 10-6
TO = 17.5 s
Calculate Total Time Delay:
TD = TO + TL
1 ms = 17.5 * 10-6 + (7.0 * 10-6 )* COUNT
1 * 10-3 = 17.5 * 10-6 + (7.0 * 10-6 )* COUNT
COUNT
Instruction | T-States
MVI C, COUNT | 7
MOV A,B | 4
OUT 01H | 10
DCR B | 4
JNZ LOOP | 10
TOTAL | 35 T
 (140)10 = (8C)16

## Slide 40: 0-9 up/down counter program
Write an 8085 assembly language program to generate a decimal counter (which counts 0 to 9 continuously) with a one second delay in between. The counter should reset itself to zero and repeat continuously. Assume a Clock frequency of 1MHz.

## Slide 41: 0-9 up counter program
Program
START: MVI B,00H
DISPLAY: OUT 01
LXI H, COUNT
LOOP: DCX H
MOV A,L
ORA H
JNZ LOOP
INR B
MOV A,B
CPI 0A
JNZ DISPLAY
JZ START
Instruction | T-States
DCX | 6
MOV A,L | 4
ORA H | 4
JNZ | 10
TOTAL | 24 T

## Slide 42: 0-9 up counter program
Delay Calculation:
As show in previous program of register pair, assuming
T-states = 24
Loop Delay TL = 1 sec
Clock Period T =1 * 10-6 sec
Find Count
TL= T * Loop T-states * Count
1 sec = (1.0 * 10-6 sec) * 24 * Count
Count =
= (41666)10
= (A2C2)16 = A2C2 h

## Slide 43: Exercise
Calculate delay in following loop, assuming clock period = 0.33s
TL= T * T-states * Count
Label | Instruction | T-states
 | LXI B, 12FF H | 10
DELAY: | DCX B | 6
 | XTHL | 16
 | XTHL | 16
 | NOP | 4
 | NOP | 4
 | MOV A,C | 4
 | ORA B | 4
 | JNZ DELAY | 10/7
Ans=102ms

## Slide 44: Exercise
Write a set of 8085 assembly language instructions to generate a 1 second delay, if the crystal frequency is 6 MHz.
Note:
Clock Frequency(Operating Frequency)=Crystal Frequency/2
Clock Period = 1/Clock Frequency

## Slide 45: Square wave program
Write a program to generate a continuous square wave with the period of 500 s with clock period of 325ns, and use bit D0 to output square wave.
500 s

## Slide 46: Square wave program
Problem Analysis
In this problem, the period of square wave is 500 s; therefore, the pulse should be ON(logic 1) for 250 s and OFF(logic 0) for remaining 250 s.
Therefore, the alternate pattern of 0/1 bits can be provided by loading Accumulator with AA h (1010 1010).
Now rotating the pattern once through each delay loop.
Bit D0 of output port is used to provide logic 0 and 1.
The delay of 250s can be easily obtained with an 8-bit delay count and one register.

## Slide 47: Square wave program
Program
MVI D, AA
ROTATE: MOV A,D
RLC
MOV D,A
ANI 01
OUT 01
MVI B, COUNT
DELAY: DCR B
JNZ DELAY
JMP ROTATE
(A) 1 0 1 0 1 0 1 0
After RLC 0 1 0 1 0 1 0 1
ANI 01h 0 0 0 0 0 0 0 1
After AND 0 0 0 0 0 0 0 1
(A) 0 1 0 1 0 1 0 1
After RLC 1 0 1 0 1 0 1 0
ANI 01h 0 0 0 0 0 0 0 1
After AND 0 0 0 0 0 0 0 0
Logic 1
Logic 0

## Slide 48: Square wave program
Delay Calculation:
In this problem, the pulse width is relatively small (250 s); therefore, to obtain accurate output pulse, we should take into account for all the T-states.
The total delay should include the delay in the loop and execution time of the instruction outside the loop.

## Slide 49: Square wave program
Delay Calculation:
No. of instruction outside the loop is seven.
Delay outside the loop TO=46 T-states * 325 ns =14.95s
Delay Loop includes two instruction, with 14 T-States, except for last cycle 11 T-States
Loop Delay TL= 14 T * 325ns * (COUNT -1) + [ 11 T *325ns ]
TL = 4.5 s (COUNT -1) + 3.575 s
Total delay required = 250 s
TD = TO + TL
250 s = 14.95s + 4.5 s (COUNT -1) + 3.575 s
Count = (52)10
= (34)16

## Slide 50: Exercise
Write a program to generate a square wave with the period of 400s with clock period of 325ns. Use bit D0 to output square wave.
ANS = (42)10