## Slide 1
PN Diode and Transistor
Unit 1
Electronics Engineering Department
DELD

## Slide 2: P – Type Semiconductor
Germanium doped with Boron (Trivalent Impurity)

## Slide 3: N – Type Semiconductor
Germanium doped with Antimony (Pentavalent Impurity)

## Slide 4: PN Junction

## Slide 5: Depletion Layer

## Slide 6: Depletion Layer
The excess electrons in the N- Region cross the junction and combine with the excess holes in the P – region.
N- Region looses electrons and becomes positively charged
P - Region looses holes and becomes negatively charged
At some point this migration stops (Concentration becomes same)
Any additional electrons from N side are repelled by the negative charge of the P – Region
Similarly, additional holes from the P side are repelled by the positive charge of the N –Region

## Slide 7: Depletion Layer Cont…
This results in a thin layer on both the sides at the junction which contains only immobile charge carriers. This is known as depletion layer. Range is in micrometers
Width depends on doping
Heavily doped – less width and vice-versa
Electrons in the N region have to climb the potential hill in order to reach the P – Region. This potential is known as Potential Barrier.
Ge – 0.3 volts, Silicon – 0.7 volts

## Slide 8: Forward Bias
Positive terminal of the battery is connected to p-region and negative terminal is connected to n-region
Width of depletion layer decreases
Current flows in the forward direction and diode acts as a short circuit

## Slide 9: Forward Characteristics

## Slide 10: Diode Equation
Is – Reverse Saturation Current
Vd is the applied Forward Biased voltage
n – Ideality Factor (if not mentioned, assume as 1)
Vt – Thermal voltage (25 milli volts at room temperature: 27 degrees/300 degree K)

## Slide 11: Reverse Bias
Positive terminal of the battery is connected to N – side and Negative terminal of the battery is connected to P – Side
The free electrons and the free holes are attracted back towards both the battery terminals
The charge carriers move away from the depletion layer
Width of depletion layer increases
No current flows and the diode acts as an open circuit

## Slide 12: Breakdown Voltage
Go on increasing the reverse bias. At certain voltage, The current increases at a very rapid rate in a direction opposite to that of the positive voltage region.
The reverse-bias potential that results in this dramatic change in characteristics is called the Breakdown Voltage.

## Slide 13: Diode Characteristics

## Slide 14: Equivalent Circuits
Ideal Diode
Diode will behave as short circuit as soon as the voltage across it becomes greater than zero

## Slide 16: Practical Diode
We must overcome the potential barrier of 0.7 volts (silicon) for a diode to make it forward bias

## Slide 17: Ideal vs. Actual Characteristics

## Slide 18: Diode as a Rectifier
Diode behaves as a switch
Forward Biased – Closed Switch, connects AC Supply to load
Reverse Biased – Open Switch, disconnects AC with load

## Slide 19: Concept Check…
Identify whether the diode/diodes is/are forward or reverse biased?

## Slide 20: Diode as a Clipper (Series)
Clipping a portion of an input signal without distorting the remaining part of the waveform

## Slide 21: Diode as a Clipper (Parallel)

## Slide 22: Concept Check…

## Slide 23: Solution

## Slide 24: Zener Diode
A special diode designed to operate in reverse breakdown region
An ordinary diode will get damaged due to excessive current
A zener diode is heavily doped to reduce the breakdown voltage as well as depletion layer width
As a result the diode has a sharp reverse breakdown voltage
Characteristics show two imp points
  After breakdown, the diode current increases rapidly
  The reverse voltage across the diode remains constant.
  This phenomenon of voltage remaining constant helps us to use Zener diode in voltage regulation.

## Slide 25: Zener Diode’s Equivalent Ckt
Always operated in reverse bias
When forward biased, will behave as a normal diode
When the reverse voltage across the diode is greater than or equal to the breakdown voltage, it can be replaced by a battery equal to the Vz (Zener Voltage or Breakdown Voltage)

## Slide 26: Zener Diode’s Equivalent Ckt
However if the reverse voltage is less than the breakdown voltage, it will work as open circuit as shown below.

## Slide 27: Zener Diode as a Regulator
Try to find the state of the zener diode (Off, Forward Biased, Reverse Biased, Reverse Biased and in Breakdown)
Remove the diode and find the voltage across Load Resistance
If above voltage is greater than specified breakdown voltage of zener diode than replace it by a battey of Vz. The voltage now across both diode as well as the Load resistance will remain constant at Vz.
If it less, then the replace it by an open circuit. In this case there is no regulation and the voltage across the load fluctuates as per the variations in the input power supply.

## Slide 28: Zener Diode as a Regulator
V > Vz: Eo = Vz, Iz = I – IL, Pz = Vz. Iz, IL = Vz/RL
V < Vz: I = IL, Iz = 0, Pz = 0 (Pz = Vz.Iz), IL = Ei/(R+RL) = I

## Slide 29: Concept Check
Determine whether Zener diode is on or off? Accordingly specify the output voltage.

## Slide 30: LED (Light Emitting Diode)
It is a diode which emits visible light when forward biased
Made from Gallium, Phosphorus or/and Arsenic (GaAs, GaPh, GaInPh). Changing the element and proportion changes the color.
Gallium Arsenide – Red Light
Gallium Phosphide – Green Light
When LED is forward biased, the electrons cross the junction and recombine with holes.
These electrons being in conduction band are at higher energy levels.
When they recombine, energy is released in the form of heat and light.
For Si and Ge diodes, the entire energy is given in the form of heat and the emitted light is insignificant.
For LED, the sufficient energy is emitted as light that too in the visible region.
Works as a normal diode when forward biased.

## Slide 31: LEDs Cont…

## Slide 32: Multi-Color LEDs
These LEDs emit one color when forward biased and another when reverse biased
Comprises of two PN-junctions connected in reverse-parallel mode.
Usually when forward biased these LEDs emit RED color and when reverse biased they emit GREEN color.
If these are switched fast between the two polarities then they emit the third color. For example RED and GREEN combination will emit Yellow as third color.

## Slide 33: Seven Segment Display

## Slide 34: SSD Cont…
LEDs are grouped to form a Seven Segment Display
It contains seven LEDs A, B, C, D, E, F and G in shape of a figure ‘8’
If a particular LED is forward biased then that LED will glow, thereby lighting up that segment or bar.
By forward biasing various combinations of these seven LEDs, it is possible to display any number between 0 – 9.

## Slide 35
Eg. When A, B, C and D are lit, (By forward biasing them), the display will show number ‘3’
To get ‘0’ all segments except ‘G’ are lit.
In figure (ii) external resistors are included to limit current thereby preventing LEDs from damage
The configuration is referred to as Common Anode type. We also have Common Cathode type SSDs.

## Slide 36: To Be Continued…