## Slide 1: Floating point Representation
-by Komal Sindhi

## Slide 2: Floating point representation
IEEE 754 floating point representation
Standard format for representing decimal floating point number into binary in 32-bits
The distribution of 32 bits is follows:
S = Sign of the number ( 1 for negative and 0 for positive)
E= 8- bit biased exponent
M= 23-bit mantissa
Sign | Exponent | Mantissa
1-bit 8-bits 23-bits

## Slide 3: IEEE 754 floating point representation
Given Number:
85. 125
STEP 1: Convert the number into binary.
Binary for 85 = 1010101
Binary for 0.125= 0.001
Final number: 1010101. 001
STEP 2: Normalize the given number such that there is a “1” before decimal point.
Normalized number: 1.010101 × 26

## Slide 4: IEEE 754 floating point representation
STEP 3: Find S
Here the number is positive. So the value of S (first bit) = 0.
STEP 4: Find biased Exponent
Exponent:+6
Biased Exponent= +6 +127= 133
Find Binary for 133= 10000101 = 8-bit Exponent E

## Slide 5: IEEE 754 floating point representation
STEP 5 : Find 23 –bit Mantissa
From the normalized number (1.010101 × 26 ) , 1 before the decimal point is implicit one. Ignore that and consider remaining bits.
Remaining bits are: 010101 -🡪 6 –bits
23 –bit Mantissa M = 01010100000000000000000.
Final Answer : SEM = 0100010101010100000000000000000.

## Slide 6: More examples:
Question : Hexadecimal notation for -14.25
Binary: 1110.01
Normalized Binary Number : 1.11001 × 23
1) S=1 because the number is negative
2) Exponent = 3 +127 =130= 10000010 (8-bit binary)
3) Mantissa: After ignoring implicit 1, 11001 is left
23- bit Mantissa= 11001000000000000000000
Final Answer: 11000001011001000000000000000000
1.11001 X 2 ^ 3

## Slide 7: Example:
Answer in Hexadecimal
1100 0001 0110 0100 0000 0000 0000 0000
C 1 6 4 0 0 0 0

## Slide 8: Examples…
Convert (-0.75) into binary
(0.11)
1.1 × 2-1
1) S= 1 (negative number)
2) Biased exponent= -1 +127 = 126 ( 01111110 in binary)
3) Mantissa: After ignoring implicit 1 , 1 is left
So M= 10000000000000000000000
Answer: 10111111010000000000000000000000

## Slide 9: Examples..
Given: 11000000101000000000000000000000
1 10000001 01000000000000000000000
1) Sign = Negative ( consider -1)
2) Biased exponent in Binary = 10000001 = 129
3) Exponent= 129-127 =2
4) Mantissa or fractional part: 0. 01000000000000000000000
                = 0.25 in decimal
5) Add implicit 1 to 0.25, So M =1 + 0.25= 1.25
Answer= (S) (E) (M) = (-1) × (22 ) × (1.25) = (-5)

## Slide 10: Examples..
Given :
0 10000011 101000000000000000000000
Find the corresponding floating point number