## Slide 1
Department of Electronics Engineering
Sardar Vallabhbhai National Institute of Technology, Ichchhanath, Surat-395 007, Gujarat
Year 2020-21
By
Prof. Naresh B. Kanirkar
Prof. Mehul C. Patel Assisted by
Arpan Shah
Digital Communication
E-Laboratory and practicals
B.Tech. II (CSE), semester –III

## Slide 2
Objective- To study of pulse code modulation (PCM) and demodulation technique.
Experiment-10

## Slide 3
PCM is a technique, which is used to convert an analog signal into digital signal.
PCM is a preferred method of communication within the public switched telephone network (PSTN)
Pulse Code Modulation (PCM)
A PCM stream is determined by two following steps:
Sampling rate- which is the number of times per second that samples are taken.
Bit depth- which determines the number of possible digital values that can be used to represent each sample.
Hence, the output of a PCM resembles a binary sequence.

## Slide 4: Why digital transmission??
Less susceptible to interference cause by noise due to discrete level.
Easy to detect errors due to discrete level.
Easy to encrypt(Higher security)
Simpler to store digital data

## Slide 6
Block diagram of PCM

## Slide 7
Sampling
Sampler extract samples of a continuous signal.
Sampler produces samples that are equivalent to the instantaneous value of the continuous signal at the specified various points.
The Sampling process generates flat- top Pulse Amplitude Modulated (PAM) signal.

## Slide 10
Quantization
Quantization is done by dividing the range of possible values of the analog samples into some different levels and assigning the center value of each level to any sample in the quantization interval.
Quantization approximates the analog sample values with the nearest quantization values.

## Slide 11
Uniformly Quantized Signal

## Slide 12
Pulse Code Modulation (PCM) is a method of converting an analog signal into a digital signal (A/D conversion).

## Slide 14
PCM produces a series of numbers or digits instead of a pulse train.
Each one of these digits, in binary code, represent the approximate amplitude of the signal sample at that instant.

## Slide 15
PCM Receiver

## Slide 17
In PCM transmitter , the signal x(t) is first passed through the low-pass filter of cut-off frequency fm Hz .
This low-pass filter blocks all the frequency components above fm Hz. This means that now the signal x(t) is band-limited to fm Hz .
The sample and hold circuit then samples this signal at the rate of fs.
Sampling frequency fs is selected sufficiently above Nyquist rate to avoid aliasing
The output from sample and hold circuit is denoted by x(nTs).
This signal x(nTs) is discrete in time and continuous in amplitude.
A q-level quantizer compares input x(nTs) with its fixed digital levels.
Quantized signal is then encoded in PCM output using encoder.
Conclusion

## Slide 20: MATLAB

## Slide 21
1. Sampling

## Slide 22
2. Quantization
% level are between vmin and vmax with difference of del
% Contain Quantized values
% Quantization process
% To make index as binary decimal so started from 0 to N
% To make quantize value in between the levels
% Display the Quantize values

## Slide 23
3. Encoding

## Slide 24
4. Demodulation